GCC-Rover-M16
Type A / Type B

Dimensions	Width	Base: 110mm / Max (wheels protruding): 125mm
	Length	Base 160mm / Max (with attachments): 225mm
	Height	Max: 120mm / Clearance at bottom with 50mm wheels: 43mm
	Weight	Net: 490g / With battery and an attachment: 660g
Wheels	Diameter	Base 30mm / Tyre (min) 32mm / Tyre (max) 50mm
	Width	Base 8.4mm / Tyre 14mm
	Steering	4 wheels independently / -90º to 90º
Power	Battery	2 cell 7.4V Li-Po battery / Charged 8.4V / Capacity 2100-2200mAh
	Motors	DC mini metal geared motor / 150/300 RPM at 6V
Speed	Max (150RPM/50mm tyre)	~ 0.5 m/s
	Max (300RPM/50mm tyre)	~ 1 m/s
Sensors	Distance	Rover type A: HC SR04 ultra sonic sensor / Rover type B: VL53L0X IR laser distance sensor
	9dof Sensor	Rover type A: GY801 (gyro l3g4200d, accelerometer adxl345) / Rover type B: MPU9250
	Camera	Pi Camera Module v2 (8 mega pixel
Controller	Main	Raspberry Pi 3